## Slide 1: Sat Nav (GNSS)
Prof Malcolm Macleod
From GPS to Galileo, but under threat

## Slide 2
Topics
What was Sat Nav designed to do?
How it works
How it has developed over 50 years
GNSS on smartphones, and the tricks they use
The proliferating applications of Sat Nav
Sat Nav’s global impact
Its weaknesses and vulnerabilities
Combatting those vulnerabilites

## Slide 3: GPS & GLONASS – the first GNSSs
The US DOD required a system to enable military platforms to find their location, and the time,
Anywhere in the world (land/ ocean/ in the air)
24/7, in any weather
Without access to any other system (e.g. communications)
Sat Nav was the only feasible solution – and was based on predecessors (e.g. TRANSIT, 1958-1960)
“Navstar GPS” started development in 1973 – first satellite launch 1978, fully operational in 1993.
The Soviet Union started GLONASS in 1976; first launch 1982.

## Slide 4: It is an extraordinary approach
The satellites are about 21,000 km up
They travel through space at about 1km/s
To work out our position to ~1m, we have to know the positions of the satellites to an accuracy of a few cm all the time.
Challenging – but it’s the only way to meet the requirements!

## Slide 5: Basic principles
1. Assume we know exactly where one satellite is and measure the range from our receiver to it. We could be anywhere on a sphere centred on the satellite.
2. If we know where 2 satellites are and measure the ranges to them. We could be anywhere on the red circle.
3. If we know where 3 satellites are and measure the ranges to them, we could be in one of two places.
This is “triangulation” (lower diagram).
To get an accurate solution we need the satellites to be in 3 well-separated directions from the receiver
But there are two problems …
User position
Alternative solution - far out in space

## Slide 6: Pseudorange
We can’t actually measure the range directly.
Every satellite carries a very accurate clock (expensive, heavy) and transmits a signal that is “timestamped” so we can work out when it was transmitted.
If we have a mathematical model of exactly where each satellite is as a function of time (its “ephemeris”) then if we also had a very accurate clock we could work out the range to it (tho’ tricky).
But the receiver doesn’t have a very accurate clock so instead of “ranges” the measurements are “pseudoranges” – which all contain the same range error due to the receiver time error.
But if we can see (at least) 4 satellites, we can work out position and accurate time, i.e. PVT (Position, Velocity, Time).

## Slide 7: The satellite orbits
Geostationary (GEO) satellites are 35.8km up. And they’re directly above the equator – not good for position fixing over the whole world.
So the satellites must be in non-GEO orbits, moving through the sky. And we require global coverage.
With 24 satellites in Middle Earth Orbit (MEO) about 22km up, we can see at least 6 satellites from anywhere on earth.
(Lower would mean the satellite could transmit less power, but would need more satellites)
The satellites are constantly moving so which ones we see change with time (11 hour orbital period).
The red lines are the ranges from the satellites to our receiver

## Slide 8: System and satellite tradeoffs
Higher orbit would imply:
Fewer satellites needed (some advantages): 
More transmit power needed (hence bigger solar panels, more heat to dissipate, bigger satellite to launch) : 
GNSS satellites have got bigger – now 2.4 tons & more powerful
Atomic clock
Block II-A GPS Satellite
Block III GPS Satellite

## Slide 9: GNSS position accuracy
The radio waves are delayed by
The troposphere (thin layer next to earth)
  Fairly easy to model
the ionosphere (60 – 2000 km)
  Much bigger delay so bigger PVT error
  Affected by Total Electron Content (TEC) which is affected by the solar wind
  Vertical delay is normally <10m, but much worse during storms due to Solar Wind …
For the earliest GPS signal (L1 C/A) the position accuracy is normally at best <10m, 95% of the time.
Block II-A GPS Satellite

## Slide 10: Improving accuracy
Increasing chip rate (from 1 Mchip/s to 10Mchip/s) increases signal bandwidth and hence accuracy. So modern 10Mchip/s signals have been added.
Ionospheric delay can be modelled and compensated for.
It is a function of the total electron content (TEC) of the ionosphere, the distance the radio wave has to travel through it, and the carrier frequency. So the TEC must be estimated.
Because the delay varies with frequency, measuring the delay at different frequencies enables the receiver to estimate TEC and correct for it. So GPS quite soon added a signal on a second frequency (L1 and L2). But this adds receiver complexity and is limited in what it can do.
Block II-A GPS Satellite

## Slide 11: Improving accuracy with Differential GNSS
Many GPS applications require better accuracy – e.g. precision agriculture, aircraft landing.
Differential GNSS uses a reference station, which sends messages to the nearby (up to 350km) user – e.g. an aircraft on the left.
The radio wave paths to the reference station and user are very close so they have nearly the same delay
The reference station’s messages to the user allow the user to correct for the delays
this must be done for all satellites in view
The history of Differential GNSS is interesting (motivated by “selective availability” – no longer)
Block II-A GPS Satellite
Raw GPS Solutions
DGPS Solutions

## Slide 12: Improving accuracy with RTK
A similar but even more accurate system is called Real Time Kinematic (RTK) positioning.
It is used for
Precise surveying
Landing aircraft on carriers
(Just being introduced) for “top” robot lawn mowers!
RTK uses carrier phase positioning which measures the carrier phase at the two receivers
It can achieve cm position accuracy
Block II-A GPS Satellite
Raw GPS Solutions
DGPS Solutions

## Slide 13: Space-Based Augmentation Systems (SBAS)
D-GNSS needs a nearby bespoke reference receiver
For applications like civil aircraft landing in fog a wide-area solution has been invented - SBAS
Monitoring stations are spread throughout a region of interest (USA in the illustration). They measure the ionospheric and other delays.
Delay correction data is computed and sent up to a geostationary satellite, which transmits it back down to any “interested” GNSS receiver.
Deployed in: USA: WAAS; Europe: EGNOS; India: GAGN; Japan: MSAS, (QZSS); Russian Federation: SDCM
Block II-A GPS Satellite
Raw GPS Solutions
DGPS Solutions

## Slide 14: Improving accuracy – Map-based navigation
Sat Navs assume that the car is on a road in its stored map. So although their raw Position estimate may not be on a road, they “snap” the position to the nearest place on the road. So their side-to-side accuracy is good due to the mapping.
Block II-A GPS Satellite
Raw GPS Solutions
DGPS Solutions
The forward-backward position error may build up along a long straight road, but it will be corrected at the next bend or junction.

## Slide 15: Ground control
There’s a huge ground control segment. This is the GPS one.
Master time – uses a constellation of atomic clocks
Large ground stations monitor all the satellites
Their orbital and clock parameters are measured – models updated
The satellites are controlled
data is sent to the satellites for them to send messages to receivers
Block II-A GPS Satellite
Block III GPS Satellite

## Slide 16: GPS modernisation and evolution
As well as the original open service (L1C/A), GPS satellites transmit on another frequency (L2) primarily to support ionospheric estimation.
They also transmit encrypted signals on L1 and L2 – military use only
Then to provide improved accuracy another signal was added on another frequency (L5), with 10 times greater chip rate.
Since 2000, additional “modernised” GPS signals are also transmitted in the same bands.
The new satellites are bigger, more versatile and last longer, soon using ion thrusters.

## Slide 17: How it’s done – a summary
The radio signal is transmitted circularly polarised (so the receiver can have any orientation)
The antenna focuses the energy onto a patch on earth but it’s huge so the received power is still very low.
To achieve high timing accuracy with low peak power we use pulse compression (as in radar).
The carrier frequency is L1 band (1.1 – 1.5GHz). It is modulated with a spread spectrum pseudo-random noise (PRN) sequence of rectangular “chips” – different for each Satellite, so separable by correlation in the Rx.
Because GNSS has to be able to operate standalone, the satellite ephemeris data is also modulated onto it.
ns
μs
20 ms
PRN
DATA SYMBOLS
CARRIER WAVE

## Slide 18: In the receiver – Acquiring and Tracking signals
The hardest task is Acquiring the signals - both the arrival time and frequency error are unknown, the latter caused by
Doppler shift (caused by the changing range to the satellite)
Errors in the frequency of the receiver’s reference oscillator
So receivers acquire signals one by one.
The computational effort of Acquisition is why traditional car Sat Navs take a long time (~1 minute) to make an initial estimate of position (if it’s changed since when it was turned off).
Once each signal is acquired, it is then continuously tracked. Receivers typically have many (>100) tracking channels.
1977 Rockwell Collins “receive the world’s first GPS satellite signal”
first-ever GPS brochure: Manpack

## Slide 19: The challenge in receiver design
The Acquisition challenge is even greater for some modern GNSS signals (which have 10 times higher chip rate, to give greater accuracy)
And greater still for the military encrypted GNSS signals
So advanced receivers (like QinetiQ’s Q40) include specialised Digital Signal Processing – to perform acquisition faster.
There is initially a lot of time ambiguity in the results, but the receiver reduces it by
Tracking each signal, then
Synchronising to the structure within the signal.
It overcomes the remaining ambiguity / uncertainty by performing a mathematical optimisation process - a Least Squared Error solution for the ranges to the satellites it is tracking.
The result is the estimate of the PVT.
DGP 500M trans
RF ASIC
QinetiQ Q40

## Slide 20: GNSS on smartphones
In high-end smartphones, assisted or augmented GNSS (A-GNS) uses the phone data link to reduce computation and speed up acquisition. There are many variants
satellite orbital data (which is needed to calculate position) and precise time are sent over the link. This greatly reduces the computation load of acquisition
In another option the smartphone just sends data to the server and the server calculates the phone position (with lots of computing power and information)

## Slide 21: Alternative Navigation Technologies (AltNav)
High-end phones may support other location services, such as
Wi-Fi positioning (for indoor use)
cell-site multilateration (using Time Difference of Arrival – TDOA)
or sometimes a hybrid positioning system.
Another type of enhancement (only just coming) uses the other sensors inside the smartphone
accelerometers, compass and barometer
plus the GNSS PVT, to make much enhanced position estimates

## Slide 22: The four GNSSs and regional systems
GPS: US controlled; fully supported and modernised
GLONASS: Russian controlled; declined to a poor state; now restored to a full system and under Putin is being revitalised and modernised
Beidou: Chinese controlled; Beidou-3 fully operational by June 2020
Galileo: European Union controlled; theoretically more accurate than the other systems; some problems getting the satellites launched; it is recently working, but not yet quite as designed.
IRNSS: Indian controlled regional system
QZSS: Japanese system designed to augment GPS receivers in Japan

## Slide 23: GNSS applications and impact
GNSS-based timing is critical for telecommunications, financial transactions.
Positioning, navigation and timing (PNT) play a critical role in land surveying, law enforcement, emergency response, precision agriculture, mining, scientific research and so on. Tachographs. Robots, drones, driverless cars.
Applications in phones: advertising, social, navigation and route finding. Gathering and exploiting position data on people.
So GNSS has huge financial, technological, social and and political impact, and is a means for states to project their power and control. For example, “loss of GPS would cost the U.S. economy $1 - $1.5 billion a day.”
GNSSs are used in all forms of transportation: space stations, aviation, maritime, rail, road and mass transit.

## Slide 24: GNSS vulnerabilities
Jamming means transmitting a signal that prevents the GNSS receiver from working.
Spoofing means transmitting “spoof” signals to deceive the receiver about its true position or the true time.
Doing this is illegal (up to 2 years in prison, unlimited fine).
GNSS is vulnerable because the signal itself is so weak.
Some lorry drivers have used jammers to block their vehicle’s tachograph. Car thieves try to overcome theft-detecting trackers.
There have been examples of GNSS receivers in a much wider area being affected by such jammers.
In the military, many weapon systems and increasingly drones rely on GNSS. So adversaries seek to jam them.

## Slide 25: GNSS interference countermeasures
Jamming countermeasures
Jammers can be detected and located.
Special antennas that reject jamming signals while letting GNSS signals through.
Digital signal processing (DSP) in advanced receivers to suppress the jamming signals.
Spoofing countermeasures
Detecting aspects of the spoofed signals that allow them to be distinguished from real satellite signals
Special antennas that allow the receiver to estimate the direction of arrival of the signals
antenna

## Slide 26: In conclusion
GNSS has developed over 50 years
We now use it for an enormous range of valuable applications
It is politically and economically key
Its growth will continue and the technology is still advancing
But that makes us vulnerable to any attacks on GNSS
Current R & D seeks to overcome the threats to GNSS and find alternative navigation technologies

## Slide 27: Thank you
mmacleod@qinetiq.com